KTM 450 Stud Kit

Installation Instructions

- Install the 4 studs into the case Allen side up, and bottom out threads. The stud only needs snugged into the case.

- Install the cylinder and head with fresh gaskets.

- Apply assembly lube on the stud threads, and then install washers and nuts.

- Torque studs in 3 passes:

    - 21 FT/LBS

    - 30 FT/LBS

    - 40 FT/LBS